USB
Arduino
programming &
power supply
MIDI
output
DIN
Meter
& LEDs
coding switch
MIDI
base
channel
Tx1
Arduino
Keyboard
Matrix
sustain
pedal, 2 pins
expression
pedal, 3 pins
push
push
back side
    volume
   control

---
Matrix to MIDI
0.1u
0.1u
blue
+5V Gnd
Gnd
A4 A5
A0 A1 A2 A3
R5
n.c.
n.c.
n.c.
n.c.
n.c.
n.c.
n.c.
n.c.
A6
R6
G1
G2
G3
G4
G5
G6
G7
G8
n.c.
analog
meter
adjust
n.c.
        PW TxRx
13 12 11 10 9 8 7 6 5 4 3 2 1 0
. . . . . .
. . . . . .
G8 G7 G6 G5 G4 G3 G2 G1
13 = G8 connected
to yellow onboard LED
Arduino
Mega 2560
52 53
50 51
48 49
46 47
44 45
42 43
40 41
38 39
36 37
34 35
32 33
30 31
28 29
26 27
24 25
22 23
Tx3 Rx3 Tx2 Rx2 Tx1 Rx1
14 15 16 17 18 19
+5V
Gnd +9V Vin
5 4
220
1k
1k
1k
1k
1k
1k
1k
1k
1k
1k
1k
1k
. . . . . .
.
11
10
9
8
7
6
5
4
3
2
1
12k
150k
22k
20k
1k
1k
1k
1k
1k
1k
1k
1k
1k
1k
Key-
board
A5
R4
A4
R3
A3
R2
A2
A1
R1
A7
R7
A8
R8
A9
R9
A10
R10
A11
R11
n.c.
ext. pedals
 6 5 4 3 2 1
1.2k

---
+ 5V 11
white
meter
orange
keyboard
VOLTCRAFT AM-49X27
270 μA
1.66 kΩ
Arduino A2 8
Arduino A3 7
6.3 mm
mono
- +
10 A0
4 PWM
sustain
pedal
n.c.
3 Gnd
coding
switch
0..9
green
push-button
black
push-button
1 Arduino 23
2 Arduino 22
Arduino A1 9
MIDI base channel
330
180
10k
22k
47k
100k
10k

---
1 Gnd
2 Arduino A5
volume
knob
3 +5V
6.3 mm
stereo
5 Arduino A4
external
expression
pedal
4 +5V (1.2k)
6 Gnd
100k
lin.

---
on
display global sensitivity
increment global sens.
meter light on
decrement global sens.
display MIDI velocity
MIDI channel select
global sensitivity
adjust
meter light on
meter light off
meter light off
decrement key sensitivity
playing
increment key sensitivity
meter light on
display key sensitivity
meter light off
half brightness
key sensitivity
adjust
blinking on
clear split point
full brightness
display MIDI velocity
keyboard split point selection
set split point
2.5 s rotary
switch stable
long pressure
button
button
note on
note off
long pressure
long pressure
long pressure
button
button
note on
note off
pressed together
note on
pressed together

---
toggle left transpose
display left
transpose
blinking on
playing
select (left) sound / preset
blinking off
send sound / preset
short pressure
1.5 seconds
short pressure
long pressure
note on